## Slide 1: - VISCUM - A New Light Weight Software Architecture of MEC
Feng Li, Sriram Sidhar, Jae Won Chung and Jamal Hadi Salim
Notes: Default cover design.

## Slide 2: Outline
Introduction
Related Work
Viscum: process level virtualization
Conclusion

## Slide 3: Mobile Edge Computing (MEC)
Mobile Cloud Computing (MCC)
  Pros:
    Offloading battery consuming computation tasks from UE to cloud;
    Supporting mobile user access complicated service in cloud;
    Providing high volume storage resources for mobile users.
  Cons:
    Introducing additional network load on both radio and core networks;
    Increasing higher latencies, data has to be sent to cloud servers.
MEC to Address Challenges on MCC
  Move cloud service to mobile edges;
  Reducing latencies and allowing interactive between service providers and customers.
  Reducing load on mobile providers’ core network and/or radio networks.

## Slide 4: Software Architecture in MEC
Fig 1 ETSI MEC Software Model

## Slide 5: ETSI Software Model
Split cloud service into edge and cloud components.
  Extra development efforts.
  Balancing between edge nodes and cloud nodes.
  Different management for edge and cloud components.
MEC Platform
  Traffic steering
  Horizontal scalability
  Virtualization technology
  Service management

## Slide 6: MEC Questions?
Where is Edge?
When will MEC be ready to host applications?
Can we gradually deploy applications on MEC as they are ready?

## Slide 7: Think small and be practical
Let’s start from the edge devices

## Slide 8: Viscum Architecture

## Slide 9: Viscum
Light weight process level virtualization
Consists of four components
  Linux Network Namespace contains applications;
  Linux Traffic Control (TC) based traffic redirector;
  A pair of Virtual Ethernet Interfaces (veth) as a pipe between two namespaces;
  Control module manages above components.
Named it Viscum to mimic the small MEC service deployed onto edge routers (hosts).

## Slide 10: Why not use full containers ?
Container overheads
  At least four more process need to be created for one service process.
  Not required for simple service deployment.
Network namespace
  Providing network resource duplication.
  Reusing existing control plane function to manager namespaces.
  Support embedded devices, or Linux distribution with old kernel release. (Redhat supports docker from 7.0, while namespace is supported from 2.6.32.

## Slide 11: Create Viscum Host
1. Create veth inside host namespace
2. Create namespace to host MEC service.
3. Create veth inside guest namespace
4. Create TC based Traffic Redirector

## Slide 12: Sample Use Case 1 : License Plate Detection
openalpr
NY, ABC 123
Reducing data to cloud from hundred kbytes to hundred bytes.
Could be done on wifi hotspot, eNodeB.
Huge saving on bill and RTT if using expensive links, e.g. satellite links
Running on AP

## Slide 13: Sample Use Case 2 : SpeedTest Server on Edge
Motivation
  Wireless link (e.g. 5G) may not be bottleneck link anymore.
  Current cloud based speed test framework may report inter-domain congestion while customer and mobile provider has more concern on wireless link congestion.
  Saturate 5G wireless link from cloud may not be a trivial task.
  Bandwidth measurement traffic is meaning less on non bottle neck links.
Viscum Solution
  Simply deploy iperf3 daemon inside a Viscum host AP.
  No new hardware, no traffic on core network, and accurately measures wireless link capacity.

## Slide 14: Conclusions
Viscum
  A light-weight software architecture for edge device MEC
  Support gradually deployment model.
  Convert any Linux based network node into MEC application servers.
  Deploy off-the-shelf software onto mobile edge nodes (e.g. WIFI hotspot, eNodeB) without software splitting.
  Reduce service delay and traffic volume in mobile providers’ core networks and/or radio access networks.
Future works
  Distributed application deployment and management
  Viscum on OpenWRT WIFI routers